## Slide 1
Status of the first NASA EV-I Project, Tropospheric
Emissions: Monitoring of Pollution (TEMPO)
Kelly Chance, Xiong Liu, Raid Suleiman Smithsonian Astrophysical Observatory
David Flittner, Jay Al-Saadi, NASA LaRC
Scott Janz, NASA GSFC
The TEMPO Science Team
The TEMPO Management Team
Ball Aerospace & Technologies Corp.
AGU Presentation A43I-01
December 12, 2013

## Slide 2
Team Member | Institution | Role | Responsibility
K. Chance | SAO | PI | Overall science development; Level 1b, H2CO, C2H2O2
X. Liu | SAO | Deputy PI | Science development, data processing; O3 profile, tropospheric O3
J. Al-Saadi | LaRC | Deputy PS | Project science development
J. Carr | Carr Astronautics | Co-I | INR Modeling and algorithm
M. Chin | GSFC | Co-I | Aerosol science
R. Cohen | U.C. Berkeley | Co-I | NO2 validation, atmospheric chemistry modeling, process studies
D. Edwards | NCAR | Co-I | VOC science, synergy with carbon monoxide measurements
J. Fishman | St. Louis U. | Co-I | AQ impact on agriculture and the biosphere
D. Flittner | LaRC | Project Scientist | Overall project development; STM; instrument cal./char.
J. Herman | UMBC | Co-I | Validation (PANDORA measurements)
D. Jacob | Harvard | Co-I | Science requirements, atmospheric modeling, process studies
S. Janz | GSFC | Co-I | Instrument calibration and characterization
J. Joiner | GSFC | Co-I | Cloud, total O3, TOA shortwave flux research product
N. Krotkov | GSFC | Co-I | NO2, SO2, UVB
M. Newchurch | U. Alabama Huntsville | Co-I | Validation (O3 sondes, O3 lidar)
R.B. Pierce | NOAA/NESDIS | Co-I | AQ modeling, data assimilation
R. Spurr | RT Solutions, Inc. | Co-I | Radiative transfer modeling for algorithm development
R. Suleiman | SAO | Co-I, Data Mgr. | Managing science data processing, BrO, H2O, and L3 products
J. Szykman | EPA | Co-I | AIRNow AQI development, validation (PANDORA measurements)
O. Torres | GSFC | Co-I | UV aerosol product, AI
J. Wang | U. Nebraska | Co-I | Synergy w/GOES-R ABI, aerosol research products
J. Leitch | Ball Aerospace | Collaborator | Aircraft validation, instrument calibration and characterization
D. Neil | LaRC | Collaborator | GEO-CAPE mission design team member
R. Martin | Dalhousie U. | Collaborator | Atmospheric modeling, air mass factors, AQI development
Chris McLinden | Environment Canada | Collaborator | Canadian air quality coordination
Michel Grutter de la Mora | UNAM, Mexico | Collaborator | Mexican air quality coordination
J. Kim | Yonsei U. | Collaborators, Science Advisory Panel | Korean GEMS, CEOS constellation of GEO pollution monitoring
C.T. McElroy | York U. Canada |  | CSA PHEOS, CEOS constellation of GEO pollution monitoring
B. Veihelmann | ESA |  | ESA Sentinel-4, CEOS constellation of GEO pollution monitoring
TEMPO science team

## Slide 3: TEMPO science overview
TEMPO Science Questions
What are the temporal and spatial variations of emissions of gases and aerosols important for air quality and climate?
How do physical, chemical, and dynamical processes determine tropospheric composition and air quality over scales ranging from urban to continental, diurnally to seasonally?
How does air pollution drive climate forcing and how does climate change affect air quality on a continental scale?
How can observations from space improve air quality forecasts and assessments?
How does intercontinental transport affect air quality?
How do episodic events, such as wild fires, dust outbreaks, and volcanic eruptions, affect atmospheric composition and air quality?
As air quality standards become more stringent, more of the US may exceed the standards.
New and transient pollution sources (e.g., vehicular traffic, oil & gas development, trans-boundary pollution) will become more important but are very difficult to monitor from ground networks.
Air quality, climate change, and energy policies must increasingly be considered together.
TEMPO measurements will provide data to help solve these national challenges.
Counties Violating Ground-level Ozone Standards

## Slide 4
Why geostationary? High temporal and spatial resolution
Hourly NO2 surface concentration and integrated column calculated by CMAQ air quality model: Houston, TX, June 22-23, 2005
June 22
Hour of Day (UTC)
June 23
LEO observations provide limited information on rapidly varying emissions, chemistry, & transport
GEO will provide observations at temporal and spatial scales highly relevant to air quality processes

## Slide 5: NO2 over Los Angeles
Courtesy T. Kurosu

## Slide 6: TEMPO science measurements
Violations of US National Ambient Air Quality Standards are primarily related to ozone (O3) and particulate matter (aerosol)
  O3 adversely impacts health and agriculture and is a greenhouse gas
  Aerosol adversely impacts health, reduces visibility, and influences climate
  Nitrogen dioxide (NO2) and sulfur dioxide (SO2) are also regulated
TEMPO measures O3, key proxies for O3 precursors (H2CO and C2H2O2 for hydrocarbons and NO2 for nitrogen oxides), SO2, and aerosol
By simultaneously measuring O3 and the precursors from which it is produced, TEMPO provides understanding of all key phases of air quality: emissions, photochemistry, and long range transport
O3
  O3 is created in the troposphere by photochemical cycles dependent on hydrocarbons and nitrogen oxides
STRATOSPHERE
TROPOSPHERE
OH
NO2
O3
H2O
NO2
OH
O2
CO
H2CO
OH
VOC
NO
SO2
Aerosol
O3

## Slide 7: TEMPO baseline products
TEMPO has a minimally-redundant measurement set for air quality.

## Slide 8: TEMPO instrument concept
Measurement technique
  Imaging grating spectrometer measuring solar backscattered Earth radiance
  Spectral band & resolution: 290-490 + 540-740 nm @ 0.6 nm FWHM, 0.2 nm sampling
  2 2-D, 2k×1k, detectors image the full spectral range for each geospatial scene
Field of Regard (FOR) and duty cycle
  Mexico City/Yucatan Peninsula to the Canadian tar/oil sands, Atlantic to Pacific
  Instrument slit aligned N/S and swept across the FOR in the E/W direction, producing a radiance map of Greater North America in one hour
Spatial resolution
  2.1 km N/S × 4.7 km E/W native pixel resolution (9.8 km2)
  Co-add/cloud clear as needed for specific data products
Standard data products and sampling rates
  Most sampled hourly, including eXceL O3 (troposphere, PBL) for selected areas
  H2CO, C2H2O2, SO2 sampled hourly (average results for ≥ 3/day if needed)
  Nominal spatial resolution 8.4 km N/S × 4.7 km E/W at center of domain (can often measure 2.1 km N/S × 4.7 km E/W)
  Measurement requirements met up to 50o for SO2, 70o SZA for other products

## Slide 9: Typical TEMPO-range spectra (from ESA GOME-1)

## Slide 10: TEMPO mission concept
Geostationary orbit, operating on a commercial telecom satellite
  NASA will arrange launch and hosting services (per Earth Venture Instrument scope)
    90-110o W preferred, 75-137o W acceptable
    Specifying satellite environment, accommodation
  Hourly measurement and telemetry duty cycle for at least ≤70o SZA
    Plan to measure up to 20 hours/day
TEMPO is low risk with significant space heritage
  All proposed TEMPO measurements have been made from low Earth orbit satellite instruments to the required precisions
  All TEMPO launch algorithms are implementations of currently operational algorithms
    NASA TOMS-type O3
    SO2, NO2, H2CO, C2H2O2 from fitting with AMF-weighted cross sections
    Absorbing Aerosol Index, UV aerosol, Rotational Raman scattering cloud
    eXceL profile/tropospheric/PBL O3 for selected geographic targets
Example higher-level products: Near-real-time pollution/AQ indices, UV index
TEMPO research products will greatly extend science and applications
  Example research products: eXceL profile O3 for broad regions; BrO from AMF-normalized cross sections; height-resolved SO2; additional cloud/aerosol products; vegetation products

## Slide 11: The view from GEO

## Slide 12: TEMPO footprint, ground sample distance and field of regard
Each 2.1 km × 4.7 km pixel is a 2K element spectrum from 290-740 nm
GEO platform selected by NASA for viewing Greater North America
2.1 km × 4.7
__________

## Slide 13: TEMPO footprint (GEO at 100º W)
For GEO at 80ºW, pixel size at 36.5ºN, 100ºW is 2.2 km × 5.2 km.
Location | N/S (km) | E/W (km) | GSA (km2)
36.5oN, 100oW | 2.11 | 4.65 | 9.8
Washington, DC | 2.37 | 5.36 | 11.9
Seattle | 2.99 | 5.46 | 14.9
Los Angeles | 2.09 | 5.04 | 10.2
Boston | 2.71 | 5.90 | 14.1
Miami | 1.83 | 5.04 | 9.0
Mexico City | 1.65 | 4.54 | 7.5
Canadian tar sands | 3.94 | 5.05 | 19.2
Assumes 2000 N/S pixels |  |  | 

## Slide 14: TEMPO hourly NO2 sweep

## Slide 15: Washington, DC coverage
Hourly!

## Slide 16: Mexico City coverage
¡Cada hora!

## Slide 17: Measurement requirements
Spatial Resolution: ~8.84×5.11 km2 or better at the center of the field of regard
Aerosol: requires smaller native pixels for cloud clearing.
NO2, H2CO, C2H2O2, SO2 are in vertical column densities (VCDs; molecules cm-2)
TEMPO STM: from GEO-CAPE STM with modifications:
  H2CO, SO2, C2H2O2: scale precision from 3 times/day to hourly
  SZA req. for H2CO & C2H2O2 is changed to 70º. Still 50º for SO2.
STM measurement requirements  Instrument requirements.
Species | Required precision | Sensitivity driver
Trop O3 | 10 ppbv | Hourly for SZA ≤ 70o
Free trop O3 | 10 ppbv | Hourly for SZA ≤ 70o
0-2 km O3 | 10 ppbv | Hourly for SZA ≤ 70o
Total O3 | 3% | Hourly for SZA ≤ 70o
NO2 | 1.0×1015 | Hourly for SZA ≤ 70o
H2CO | 1.0×1016 1.73×1016 | 3/day for SZA ≤ 70o or Hourly for SZA ≤ 70o
SO2 | 1.0×1016 1.73×1016 | 3/day for SZA ≤ 50o or Hourly for SZA ≤ 50o
C2H2O2 | 4.0×1014 6.98×1014 | 3/day for SZA ≤ 70o or Hourly for SZA ≤ 70o
AOD | 0.10 | Hourly for SZA ≤ 70o

## Slide 18: Refinement of instrument SNR requirements
Sensitivity studies quantify variation of trace gas performance with respect to variables including SZA, time, location, cloudiness, aerosol loading, terrain height, etc.
Synthetic dataset developed from state-of-the-art (GEOS-Chem) model fields
  Hourly over TEMPO field of regard for 12 days (1 day/month) up to SZA 80°  ~90000 simulations
  O3, NO2, H2CO, SO2, C2H2O2, H2O, BrO, OClO, O2, O4
  6 types of aerosols, water/ice clouds, pixel independent approximation
  Koelemeijer GOME surface albedo database with linear interpolation
  Actual viewing geometry for a geostationary satellite (e.g., 100°W)
RTM Calculation and Sensitivity Calculation
  270-800 nm at 0.6 nm FWHM, 0.2 nm sampling
  Include additional weighting functions with respect to AOD, ASSA, COD, cloud fraction
  State vector includes AOD, ASSA, COD, cloud fraction additionally
  TEMPO SNR model: account for optical transmission and grating efficiency, including shot, dark current, RTN, readout, quantization, smear, CTE noise terms

## Slide 19: SNR requirements and instrument performance
The current TEMPO design meets SNR requirements for nominal radiances with >20% EOL margin.
Species | Spectral range (nm) | Nominal radiance phot s-1 cm-2 nm-1 sr-1 | Req’d. SNR | Actual SNR | EOL margin
O3 | 290-300 | 6.74×1010 | 48.2 | 64.2 | 33.3%
O3 | 300-345 | 7.07×1012 | 1134 | 1512 | 33.3%
O3 | 540-650 | 1.19×1013 | 1327 | 1769 | 33.3%
SO2 | 305-345 | 7.93×1012 | 1399 | 1683 | 20.3%
H2CO | 327-356 | 1.25×1013 | 763 | 2277 | 198%
Cloud | 346-354 | 1.26×1013 | 1200 | 2265 | 88.8%*
AOD | 354-388 | 1.25×1013 | 1414 | 2213 | 56.5%**
NO2 | 423-451 | 1.65×1013 | 963 | 2609 | 171%
C2H2O2 | 420-465 | 1.74×1013 | 1897 | 2629 | 38.6%
Vegetation | 700-740 | 1.36×1013 |  | 923 | 
* SNR of 600 is needed at native resolution of ~2.2×5.1 km2 |  |  |  |  | 
** SNR of 1000 is needed at native resolution using OMI UV aerosol algorithm (354+388 nm) |  |  |  |  | 

## Slide 20
Global pollution monitoring constellation (2018-2020)
Policy-relevant science and environmental services enabled by common observations
Improved emissions, at common confidence levels, over industrialized Northern Hemisphere
Improved air quality forecasts and assimilation systems
Improved assessment, e.g., observations to support United Nations Convention on Long Range Transboundary Air Pollution
Sentinel-5P
(once per day)
TEMPO
(hourly)
Sentinel-4
(hourly)
GEMS
(hourly)
Courtesy Jhoon Kim,
Andreas Richter

## Slide 21: Science summary
The TEMPO mission addresses NASA’s Strategic Plan:
  Strategic Goal 2: Expand scientific understanding of the Earth and the universe in which we live
    Advance Earth system science to meet the challenges of climate and environmental change
The science objectives of the mission lead to specific mission, measurement, and instrument requirements
The existing TEMPO mission meets these Level 1 requirements
Have defined Baseline and Threshold science requirements
The project science team, instrument team, mission team and PI are working closely together to have a successful mission.

## Slide 22: The End!

## Slide 23: Backups

## Slide 24: Process to determine and verify instrument requirements
Measurement Requirements
(STM, ISD)
Retrieval Performance
Instrument Design
RTM & Ret. Sens. vs. SNR and FWHM
RTM & Ret. Sens.
Verify
Initialize
Refine

## Slide 25: Gas retrievals: Requirements and sensitivities
TEMPO baseline measurement requirements
Methodology of sensitivity studies
Initial determination of instrument SNR requirements
Trace gas retrieval performance and refinement of SNR requirements

## Slide 26
Retrieval sensitivity studies
Perform radiative transfer model (RTM) simulations with VLIDORT: Radiances and weighting functions
Estimate retrieval errors for both O3 profile and other trace gas VCDs using the optimal estimation formulation, accounting for interferences but ignoring spectroscopic errors
  Measurement: spectral resolution, spectral interval
  Measurement error: assumed or from instrument SNR model
  State vector: target, interfering gases, Ring, surface albedo (up to 4th order)
  A priori error: climatological for O3, unconstrained for other trace gas VCDs, consistent with current algorithms
  Retrieval errors: use solution errors (smoothing + precision)
  Can calculate errors due to other parameters (e.g., radiance errors, polarization sensitivity, surface albedo, cloud, aerosol, surface pressure) for determining retrieval error budgets and calibration requirements.
Same as NLLS for VCDs (unconstrained)

## Slide 27
Initial determination of
SNR requirements
Molecule | O3 | SO2 | NO2 | H2CO | C2H2O2
Fit Windows (nm) | 290-345 540-650 | 305-330 305-345 | 423-451 | 327-356 | 433-465 420-465
Use 1 “tough” atmospheric profile under highly ideal conditions
  GSFC NY12 from K. Pickering for July
  Clear-sky, no aerosols, 0.03 surface albedo at all wavelengths
Define worst viewing scenarios (different for different trace gases)
  O3, SO2: SZA 50°, VZA 66.2° (Northwest corner, 130°W, 50°N)
  NO2: SZA 70°, VZA 17.6° (95°W, 15°N)
  H2CO, C2H2O2: SZA 50°, VZA 17.6° (95°W, 15°N)
Perform high-resolution RTM calculations: convolved to various spectral resolution and sampled at different spectral intervals.
Perform retrieval sensitivity studies: retrieval errors vs. various SNRs (shot noise only, SNR ~ SQRT(I)) and spectral resolutions

## Slide 28
Initial determination of
SNR requirements
0-2 km O3, UV
0-2 km O3, UV+Vis
NO2
SO2

## Slide 29: Determination of nominal and maximum radiances
Nominal: mean clear (fc < 0.05) over land
Maximum: maximum at each wavelength of all simulations
Saturation req.: No saturation at 50% of max radiance
Nominal and maximum radiances are often needed for instrument design to determine the radiance and saturation level and to estimate SNR

## Slide 30: O3 (0-2 km) retrieval performance (cloud fraction < 0.1)
UV
UV+Vis
For O3, measuring 0-2 km ozone to better than 10 ppbv is the driving requirement.
Not every retrieval can meet the requirement, define “requirement met” using a threshold: e.g., 90%, 95%
95% level: performance level (e.g., in error) for 95% of the cases
Use 95% except for SO2 which is 90%
SZA requirement

## Slide 31: Trace gas retrieval performance (cloud fraction < 0.1)
NO2
H2CO
SO2
C2H2O2
NO2 meets reqs. at native spatial res. for SZA up to 80°
H2CO meet requirements hourly for SZA up to 80°
SO2 is the driver

## Slide 32: Trace gas retrieval performance (cloud fraction < 0.1)
Species | Required precision | Meet reqs (%) | 95% | 90%
Trop O3 | 10 ppbv | 99.75 | 8.97 | 8.44
Free trop O3 | 10 ppbv | 87.42 | 10.96 | 10.30
0-2 km O3 | 10 ppbv | 82.84 | 11.30 | 10.56
Total O3 | 3% | 100.0 | 1.01 | 0.91
Trop O3 (UV+Vis) | 10 ppbv | 100.0 | 6.29 | 5.92
Free trop O3 (UV+Vis) | 10 ppbv | 99.70 | 8.41 | 7.92
0-2 km O3 (UV+Vis) | 10 ppbv | 98.74 | 9.10 | 8.61
Total O3 (UV+Vis) | 3% | 100.0 | 0.58 | 0.54
NO2 | 1.0×1015 | 98.51 | 6.00×1014 | 4.55×1014
H2CO | 1.73×1016 | 99.98 | 6.41×1015 | 5.74×1015
SO2 | 1.73×1016 | 95.62 | 1.68×1016 | 1.44×1016
C2H2O2 | 6.93×1014 | 99.78 | 5.02×1014 | 4.54×1014

## Slide 33: Refining SNR requirements
Select cases (~21) with retrieval errors closest to the threshold level (90% for SO2, 95% for other species )
Adjust/scale SNR over the fitting window so that worst case error matches the requirement. The adjusted SNR is the required SNR.

## Slide 34: Satellite observations of ozone precursors: Formation sensitivity of surface ozone
Ratio indicates whether O3 control strategies should focus on nitrogen oxide or hydrocarbon emissions.
Simultaneous measurements of O3, NO2 and HCHO allow distinction between local sources of O3 and trans-boundary transport.
This view is a 1-month snapshot valid at the Aura overpass time (~1:30 in the afternoon) but the indicator varies widely throughout the day. Hourly geostationary observations will provide data needed for the next generation of control strategies.
Natural VOCs from trees are so high in the East that ozone production is primarily controlled by reducing NOx emissions.
Ozone production is controlled by reducing VOC emissions in downtown LA.
Reduce NOx Emissions
Reduce VOC Emissions
Transition
Duncan et al., Atmospheric Environment, 2010
The OMI formaldehyde (HCHO) to nitrogen dioxide (NO2) ratio for August 2005

## Slide 35: TEMPO science measurements
11/12/13
35
Ozone (O3) is created in the troposphere by photochemical cycles dependent upon concentrations of hydrocarbons and nitrogen oxides
By simultaneously measuring O3 and the precursors from which it is produced, TEMPO provides understanding of all key phases of air quality: emissions, photochemistry, and long range transport
TEMPO measures O3 and key proxies for its precursor hydrocarbons (H2CO) and nitrogen oxides (NO2)
O3
STRATOSPHERE
TROPOSPHERE
OH
NO2
O3
H2O
NO2
OH
O2
CO
NO
VOC
H2CO
OH

## Slide 36: GOME-1 spectra
What do we measure?
GOME irradiance, radiance, and albedo spectrum for high-albedo (fully cloudy) ground pixel

## Slide 37: TEMPO science questions
What are the temporal and spatial variations of emissions of gases and aerosols important for air quality and climate?
How do physical, chemical, and dynamical processes determine tropospheric composition and air quality over scales ranging from urban to continental, diurnally to seasonally?
How does air pollution drive climate forcing and how does climate change affect air quality on a continental scale?
How can observations from space improve air quality forecasts and assessments for societal benefit?
How does intercontinental transport affect air quality?
How do episodic events, such as wild fires, dust outbreaks, and volcanic eruptions, affect atmospheric composition and air quality?

## Slide 38: TEMPO