## Slide 1
TEMPO Status
Kelly Chance
AQAST 7 meeting
June 17, 2014

## Slide 2: Hourly atmospheric pollution from geostationary Earth orbit
PI: Kelly Chance, Smithsonian Astrophysical Observatory
Instrument Development: Ball Aerospace
Project Management: NASA LaRC
Other Institutions: NASA GSFC, NOAA, EPA, NCAR, Harvard, UC Berkeley, St. Louis U, U Alabama Huntsville, U Nebraska, RT Solutions, Carr Astronautics
International collaboration: Korea, Europe, Canada, Mexico
Selected Nov. 2012 as NASA’s first Earth Venture Instrument
  Instrument delivery May 2017
  NASA will arrange hosting on commercial geostationary communications satellite with launch expected NET 11/2018
Provides hourly daylight observations to capture rapidly varying emissions & chemistry important for air quality
  UV/visible grating spectrometer to measure key elements in tropospheric ozone and aerosol pollution
  Exploits extensive measurement heritage from LEO missions
  Distinguishes boundary layer from free tropospheric & stratospheric ozone
Aligned with Earth Science Decadal Survey recommendations
  Makes many of the GEO-CAPE atmosphere measurements
  Responds to the phased implementation recommendation of GEO-CAPE mission design team
  North American component of an international constellation for air quality observations

## Slide 3: The view from GEO

## Slide 4: Typical TEMPO-range spectra (from ESA GOME-1)

## Slide 5: TEMPO footprint, ground sample distance and field of regard
Each 2.1 km × 4.7 km pixel is a 2K element spectrum from 290-740 nm
GEO platform selected by NASA for viewing Greater North America
2.1 km × 4.7
__________

## Slide 6: TEMPO hourly NO2 sweep

## Slide 7: TEMPO footprint (GEO at 100º W)
For GEO at 80ºW, pixel size at 36.5ºN, 100ºW is 2.2 km × 5.2 km.
Location | N/S (km) | E/W (km) | GSA (km2)
36.5oN, 100oW | 2.11 | 4.65 | 9.8
Washington, DC | 2.37 | 5.36 | 11.9
Seattle | 2.99 | 5.46 | 14.9
Los Angeles | 2.09 | 5.04 | 10.2
Boston | 2.71 | 5.90 | 14.1
Miami | 1.83 | 5.04 | 9.0
Mexico City | 1.65 | 4.54 | 7.5
Canadian tar sands | 3.94 | 5.05 | 19.2
Assumes 2000 N/S pixels |  |  | 

## Slide 8: TEMPO baseline products
TEMPO has a minimally-redundant measurement set for air quality.
Near-real time products will allow for pollution alerts, chemical weather, app-based local air quality.

## Slide 9
Why geostationary? High temporal and spatial resolution
Hourly NO2 surface concentration and integrated column calculated by CMAQ air quality model: Houston, TX, June 22-23, 2005
June 22
Hour of Day (UTC)
June 23
LEO observations provide limited information on rapidly varying emissions, chemistry, & transport
GEO will provide observations at temporal and spatial scales highly relevant to air quality processes

## Slide 10: NO2 over Los Angeles
Courtesy T. Kurosu

## Slide 11: Washington, DC coverage
Hourly!

## Slide 12: Mexico City coverage
¡Cada hora!

## Slide 13: www.epa.gov/rsig
TEMPO will use the EPA’s Remote Sensing Information Gateway (RSIG) for subsetting, visualization, and product distribution – to make TEMPO YOUR instrument

## Slide 14: TEMPO Summary
TEMPO is a pathfinder for NASA
  The first mission under the stringently cost-capped Earth Venture Instrument program
  First use of a competitively selected commercial host satellite
Currently on-schedule and on-budget
  Passed System Requirements Review and Mission Definition Review in November 2013
  Passed KDP-B April 2014, now in Phase B
  Most technical issues solved at the preliminary design level, following technical interchange meeting at Ball, April 2014
  PDR scheduled for late July 2014
Commercial satellite host selection and Instrument CDR summer 2015
  TEMPO operating longitude and launch date are not known until after host selection
Instrument delivery 05/2017 for launch no earlier than 11/2018

## Slide 15: The End!

## Slide 16: Backups

## Slide 17
Species/Products | Required Precision | Temporal Revisit
0-2 km O3 Selected Scenes, Baseline only | 10 ppbv | 2 hour
Tropospheric O3 | 10 ppbv | 1 hour
Total O3 | 3% | 1 hour
Tropospheric NO2 | 1.0 × 1015 molecules cm-2 | 1 hour
Tropospheric H2CO | 1.0 × 1016 molecules cm-2 | 3 hour
*Tropospheric SO2 | 1.0 × 1016 molecules cm-2 | 3 hour
*Tropospheric C2H2O2 | 4.0 × 1014 molecules cm-2 | 3 hour
*Aerosol Optical Depth | 0.10 | 1 hour
Minimal set of products sufficient for constraining air quality
Field of Regard (FOR) is Greater North America, depending on host satellite selected:
  At least 19°N to 57.5°N near 100°W
  At least 67°W to 125°W near 42°N
Data products at urban-regional spatial scales
  Baseline ≤ 60 km2 at center of FOR
  Capability for retrieval at native pixel resolution (approx. 2.1 km x 4.7 km) when SNR allows
Geolocation uncertainty of less than 4 km
Temporal scales to resolve diurnal changes in pollutant distributions
Mission duration, subject to instrument availability
  Baseline 20 months
  Threshold 12 months
*Implementation of SO2, C2H2O2, and aerosol algorithms is deferred until after successful instrument PDR
Likely ~October 2015
No impact on instrument design capability
All products still ready for launch once approved
Baseline and threshold
data products

## Slide 18: TEMPO Science Traceability Matrix

## Slide 19
Team Member | Institution | Role | Responsibility
K. Chance | SAO | PI | Overall science development; Level 1b, H2CO, C2H2O2
X. Liu | SAO | Deputy PI | Science development, data processing; O3 profile, tropospheric O3
J. Al-Saadi | LaRC | Deputy PS | Project science development
J. Carr | Carr Astronautics | Co-I | INR Modeling and algorithm
M. Chin | GSFC | Co-I | Aerosol science
R. Cohen | U.C. Berkeley | Co-I | NO2 validation, atmospheric chemistry modeling, process studies
D. Edwards | NCAR | Co-I | VOC science, synergy with carbon monoxide measurements
J. Fishman | St. Louis U. | Co-I | AQ impact on agriculture and the biosphere
D. Flittner | LaRC | Project Scientist | Overall project development; STM; instrument cal./char.
J. Herman | UMBC | Co-I | Validation (PANDORA measurements)
D. Jacob | Harvard | Co-I | Science requirements, atmospheric modeling, process studies
S. Janz | GSFC | Co-I | Instrument calibration and characterization
J. Joiner | GSFC | Co-I | Cloud, total O3, TOA shortwave flux research product
N. Krotkov | GSFC | Co-I | NO2, SO2, UVB
M. Newchurch | U. Alabama Huntsville | Co-I | Validation (O3 sondes, O3 lidar)
R.B. Pierce | NOAA/NESDIS | Co-I | AQ modeling, data assimilation
R. Spurr | RT Solutions, Inc. | Co-I | Radiative transfer modeling for algorithm development
R. Suleiman | SAO | Co-I, Data Mgr. | Managing science data processing, BrO, H2O, and L3 products
J. Szykman | EPA | Co-I | AIRNow AQI development, validation (PANDORA measurements)
O. Torres | GSFC | Co-I | UV aerosol product, AI
J. Wang | U. Nebraska | Co-I | Synergy w/GOES-R ABI, aerosol research products
J. Leitch | Ball Aerospace | Collaborator | Aircraft validation, instrument calibration and characterization
D. Neil | LaRC | Collaborator | GEO-CAPE mission design team member
R. Martin | Dalhousie U. | Collaborator | Atmospheric modeling, air mass factors, AQI development
Chris McLinden | Environment Canada | Collaborator | Canadian air quality coordination
Michel Grutter de la Mora | UNAM, Mexico | Collaborator | Mexican air quality coordination
J. Kim | Yonsei U. | Collaborators, Science Advisory Panel | Korean GEMS, CEOS constellation of GEO pollution monitoring
C.T. McElroy | York U. Canada |  | CSA PHEOS, CEOS constellation of GEO pollution monitoring
B. Veihelmann | ESA |  | ESA Sentinel-4, CEOS constellation of GEO pollution monitoring
TEMPO science team

## Slide 20: Meeting emphasis
TEMPO science studies during and after commissioning
Fluorescence
Lightning NOx
Soil NOx
NO/NO2 at high dawn and dusk time resolution
Forest fires at high time resolution
Subsampling and spatial resolution


## Slide 21
Global pollution monitoring constellation (2018-2020)
Policy-relevant science and environmental services enabled by common observations
Improved emissions, at common confidence levels, over industrialized Northern Hemisphere
Improved air quality forecasts and assimilation systems
Improved assessment, e.g., observations to support United Nations Convention on Long Range Transboundary Air Pollution
Sentinel-5P
(once per day)
TEMPO
(hourly)
Sentinel-4
(hourly)
GEMS
(hourly)
Courtesy Jhoon Kim,
Andreas Richter

## Slide 22: Baseline and Threshold Data Products
Species/Products | Required Precision | Temporal Revisit
0-2 km O3 (Selected Scenes) Baseline only | 10 ppbv | 2 hour
Tropospheric O3 | 10 ppbv | 1 hour
Total O3 | 3% | 1 hour
Tropospheric NO2 | 1.0 × 1015 molecules cm-2 | 1 hour
Tropospheric H2CO | 1.0 × 1016 molecules cm-2 | 3 hour
Tropospheric SO2 | 1.0 × 1016 molecules cm-2 | 3 hour
Tropospheric C2H2O2 | 4.0 × 1014 molecules cm-2 | 3 hour
Aerosol Optical Depth | 0.10 | 1 hour
PLRA Table 1
Minimal set of products sufficient for constraining air quality
Across Greater North America (GNA): 18°N to 58°N near 100°W, 67°W to 125°W near 42°N
Data products at urban-regional spatial scales
  Baseline ≤ 60 km2 at center of Field Of Regard (FOR)
  Threshold ≤ 300 km2 at center of FOR
Temporal scales to resolve diurnal changes in pollutant distributions
Collected in cloud-free scenes
Geolocation uncertainty of less than 4 km
Mission duration, subject to instrument availability
  Baseline 20 months
  Threshold 12 months

## Slide 23: Data Product Definitions and Details
Data Product | Description | Time beyond on-orbit checkout to deliver initial data | Maximum data latency after first release for ≥ 80% of all products†
Level 0 | Reconstructed, Unprocessed Instrument Data | 2 months | Within 2 hours of receipt at SAO
Level 1b | Calibrated, Geolocated Radiances | 4 months | Within 3 hours of Level 0 and ancillary data receipt at SAO
Level 2 | Derived Geophysical Data Products | 6 months | Within 24 hours of production of Level 1 at SAO
Level 3 | Derived Gridded Geophysical Data Products | 6 months | 1 month after completion of data accumulation required for individual geophysical products
All original observation data and standard science data products listed here, along with the scientific source code for algorithm software, coefficients, and ancillary data used to generate these products, shall be delivered to the designated NASA SMD/ESD-assigned DAAC within six months of completion of the prime mission. Data products are publicly distributed during the mission.
†80% of the products, not 80% of the product types, will be produced within this latency time.

## Slide 24: TEMPO