## Slide 1
Implementation of Tropospheric Emissions: Monitoring of
Pollution (TEMPO)
Kelly Chance, Xiong Liu,
Raid M. Suleiman,
Smithsonian Astrophysical
Observatory
David Flittner, Jay Al-Saadi,
NASA LaRC
Scott Janz, NASA GSFC
5th GEMS Science
Team Meeting
7 October 2014

## Slide 2: Hourly atmospheric pollution from geostationary Earth orbit
PI: Kelly Chance, Smithsonian Astrophysical Observatory
Instrument Development: Ball Aerospace
Project Management: NASA LaRC
Other Institutions: NASA GSFC, NOAA, EPA, NCAR, Harvard, UC Berkeley, St. Louis U, U Alabama Huntsville, U Nebraska, RT Solutions, Carr Astronautics
International collaboration: Korea, U.K., ESA, Canada, Mexico
Selected Nov. 2012 as NASA’s first Earth Venture Instrument
  Instrument delivery May 2017
  NASA will arrange hosting on commercial geostationary communications satellite with launch expected NET 11/2018
Provides hourly daylight observations to capture rapidly varying emissions & chemistry important for air quality
  UV/visible grating spectrometer to measure key elements in tropospheric ozone and aerosol pollution
  Exploits extensive measurement heritage from LEO missions
  Distinguishes boundary layer from free tropospheric & stratospheric ozone
Aligned with Earth Science Decadal Survey recommendations
  Makes many of the GEO-CAPE atmosphere measurements
  Responds to the phased implementation recommendation of GEO-CAPE mission design team
  North American component of an international constellation for air quality observations

## Slide 3: TEMPO instrument project detailed organization structure
TEMPO Instrument
Principal Investigator: Kelly Chance
Deputy Principal Investigator: Xiong Liu
Program Administrator: Joseph Webber
Investigation Advisory Panel
SAO: Roger Brissenden, LaRC: Steve Jurczyk, Ball: Mark Bergeland
Project Management
Project Manager: Wendy Pennington
Project Scientist: David Flittner
Deputy PS: Jay Al-Saadi
Deputy PM: Craig Jones, COR
Deputy PP&C: Don Shick
Instrument
PM Dennis Nicks
Chief SE: Laura Hale
Instrument Performance: Brian Baker
Systems Engineering
Project CE: David Rosenbaum
SE: Mark Andraschko
Safety & Mission Assurance
Mission Assurance Manager: Jose Caraballo
Science Team
Instrument Operations
Raid M. Suleiman
Science Advisory Panel
Geo Constellation/CEOS
Ground
Systems
Raid M. Suleiman
Science Data Processing System
Kelly Chance
Management Support
Schedules: Bonnie Lahiff
Configuration Manager: Donna Lewis
Communications: Jonathan Behun/Katie Bethea

## Slide 4
Team Member | Institution | Role | Responsibility
K. Chance | SAO | PI | Overall science development; Level 1b, H2CO, C2H2O2
X. Liu | SAO | Deputy PI | Science development, data processing; O3 profile, tropospheric O3
J. Al-Saadi | LaRC | Deputy PS | Project science development
J. Carr | Carr Astronautics | Co-I | INR Modeling and algorithm
M. Chin | GSFC | Co-I | Aerosol science
R. Cohen | U.C. Berkeley | Co-I | NO2 validation, atmospheric chemistry modeling, process studies
D. Edwards | NCAR | Co-I | VOC science, synergy with carbon monoxide measurements
J. Fishman | St. Louis U. | Co-I | AQ impact on agriculture and the biosphere
D. Flittner | LaRC | Project Scientist | Overall project development; STM; instrument cal./char.
J. Herman | UMBC | Co-I | Validation (PANDORA measurements)
D. Jacob | Harvard | Co-I | Science requirements, atmospheric modeling, process studies
S. Janz | GSFC | Co-I | Instrument calibration and characterization
J. Joiner | GSFC | Co-I | Cloud, total O3, TOA shortwave flux research product
N. Krotkov | GSFC | Co-I | NO2, SO2, UVB
M. Newchurch | U. Alabama Huntsville | Co-I | Validation (O3 sondes, O3 lidar)
R.B. Pierce | NOAA/NESDIS | Co-I | AQ modeling, data assimilation
R. Spurr | RT Solutions, Inc. | Co-I | Radiative transfer modeling for algorithm development
R. Suleiman | SAO | Co-I, Data Mgr. | Managing science data processing, BrO, H2O, and L3 products
J. Szykman | EPA | Co-I | AIRNow AQI development, validation (PANDORA measurements)
O. Torres | GSFC | Co-I | UV aerosol product, AI
J. Wang | U. Nebraska | Co-I | Synergy w/GOES-R ABI, aerosol research products
J. Leitch | Ball Aerospace | Collaborator | Aircraft validation, instrument calibration and characterization
D. Neil | LaRC | Collaborator | GEO-CAPE mission design team member
R. Martin | Dalhousie U. | Collaborator | Atmospheric modeling, air mass factors, AQI development
Chris McLinden | Environment Canada | Collaborator | Canadian air quality coordination
Michel Grutter de la Mora | UNAM, Mexico | Collaborator | Mexican air quality coordination
Brian Kerridge | Rutherford Appleton Laboratory, UK | Collaborator | Ozone profiling studies, algorithm development
Paul Palmer | Edinburgh U., UK | Collaborator | Atmospheric modeling, process studies
J. Kim | Yonsei U. | Collaborators, Science Advisory Panel | Korean GEMS, CEOS constellation of GEO pollution monitoring
C.T. McElroy | York U. Canada |  | CSA PHEOS, CEOS constellation of GEO pollution monitoring
B. Veihelmann | ESA |  | ESA Sentinel-4, CEOS constellation of GEO pollution monitoring
TEMPO science team

## Slide 5: TEMPO mission project integrated master schedule

## Slide 6: The view from GEO

## Slide 7: TEMPO instrument concept
Measurement technique
  Imaging grating spectrometer measuring solar backscattered Earth radiance
  Spectral band & resolution: 290-490 + 540-740 nm @ 0.6 nm FWHM, 0.2 nm sampling
  2 2-D, 2k×1k, detectors image the full spectral range for each geospatial scene
Field of Regard (FOR) and duty cycle
  Mexico City/Yucatan Peninsula to the Canadian tar/oil sands, Atlantic to Pacific
  Instrument slit aligned N/S and swept across the FOR in the E/W direction, producing a radiance map of Greater North America in one hour
Spatial resolution
  2.1 km N/S × 4.7 km E/W native pixel resolution (9.8 km2)
  Co-add/cloud clear as needed for specific data products
Standard data products and sampling rates
  Most sampled hourly, including eXceL O3 (troposphere, PBL) for selected areas
  H2CO, C2H2O2, SO2 sampled hourly (average results for ≥ 3/day if needed)
  Nominal spatial resolution 8.4 km N/S × 4.7 km E/W at center of domain (can often measure 2.1 km N/S × 4.7 km E/W)
  Measurement requirements met up to 50o for SO2, 70o SZA for other products

## Slide 8: Instrument layout
Calibration Mechanism Assembly
Telescope Assembly
Spectrometer Assembly
Scan Mechanism Assembly
Focal Plane
Assembly
Focal Plane Electronics
Instrument Support
Assembly
Radiator Assembly
Instrument
Control Electronics

## Slide 9: Typical TEMPO-range spectra (from ESA GOME-1)

## Slide 10: Algorithm testing: OMPS H2CO
OMPS slant column H2CO monthly average for July 2012. Because of higher SNR, the OMPS precisions are substantially higher than those from OMI.

## Slide 11: Algorithm testing: OMPS NO2
OMPS tropospheric slant column NO2 for July 2-7, 2012. Much optimization remains to improve fitting and remove artifacts but the data are nearly of sufficient quality for scientific studies. The SAA is readily visible.

## Slide 12: TEMPO mission concept
Geostationary orbit, operating on a commercial telecom satellite
  NASA will arrange launch and hosting services (per Earth Venture Instrument scope)
    80-115o W acceptable latitude
    Specifying satellite environment, accommodation
  Hourly measurement and telemetry duty cycle for at least ≤70o SZA
    Hope to measure up to 20 hours/day
TEMPO is low risk with significant space heritage
  All proposed TEMPO measurements have been made from low Earth orbit satellite instruments to the required precisions
  All TEMPO launch algorithms are implementations of currently operational algorithms
    NASA TOMS-type O3
    SO2, NO2, H2CO, C2H2O2 from fitting with AMF-weighted cross sections
    Absorbing Aerosol Index, UV aerosol, Rotational Raman scattering cloud
    eXceL profile/tropospheric/PBL O3 for selected geographic targets
Example higher-level products: Near-real-time pollution/AQ indices, UV index
TEMPO research products will greatly extend science and applications
  Example research products: eXceL profile O3 for broad regions; BrO from AMF-normalized cross sections; height-resolved SO2; additional cloud/aerosol products; vegetation products

## Slide 13: TEMPO footprint, ground sample distance and field of regard
Each 2.1 km × 4.7 km pixel is a 2K element spectrum from 290-740 nm
GEO platform selected by NASA for viewing Greater North America
2.1 km × 4.7
__________

## Slide 14: TEMPO hourly NO2 sweep

## Slide 15: TEMPO footprint (GEO at 100º W)
For GEO at 80ºW, pixel size at 36.5ºN, 100ºW is 2.2 km × 5.2 km.
Location | N/S (km) | E/W (km) | GSA (km2)
36.5oN, 100oW | 2.11 | 4.65 | 9.8
Washington, DC | 2.37 | 5.36 | 11.9
Seattle | 2.99 | 5.46 | 14.9
Los Angeles | 2.09 | 5.04 | 10.2
Boston | 2.71 | 5.90 | 14.1
Miami | 1.83 | 5.04 | 9.0
Mexico City | 1.65 | 4.54 | 7.5
Canadian tar sands | 3.94 | 5.05 | 19.2
Assumes 2000 N/S pixels |  |  | 

## Slide 16: TEMPO baseline products
TEMPO has a minimally-redundant measurement set for air quality.
Near-real time products will allow for pollution alerts, chemical weather, app-based local air quality.
Revised PLRA has O3, NO2, H2CO as baseline

## Slide 17
Why geostationary? High temporal and spatial resolution
Hourly NO2 surface concentration and integrated column calculated by CMAQ air quality model: Houston, TX, June 22-23, 2005
June 22
Hour of Day (UTC)
June 23
LEO observations provide limited information on rapidly varying emissions, chemistry, & transport
GEO will provide observations at temporal and spatial scales highly relevant to air quality processes

## Slide 18: NO2 over Los Angeles
Courtesy T. Kurosu

## Slide 19: Washington, DC coverage
Hourly!

## Slide 20: Mexico City coverage
¡Cada hora!

## Slide 21
Global pollution monitoring constellation (2018-2020)
Policy-relevant science and environmental services enabled by common observations
Improved emissions, at common confidence levels, over industrialized Northern Hemisphere
Improved air quality forecasts and assimilation systems
Improved assessment, e.g., observations to support United Nations Convention on Long Range Transboundary Air Pollution
Sentinel-5P
(once per day)
TEMPO
(hourly)
Sentinel-4
(hourly)
GEMS
(hourly)
Courtesy Jhoon Kim,
Andreas Richter

## Slide 22: www.epa.gov/rsig
TEMPO will use the EPA’s Remote Sensing Information Gateway (RSIG) for subsetting, visualization, and product distribution – to make TEMPO YOUR instrument

## Slide 23: TEMPO summary
Currently on-schedule and on-budget
  Passed System Requirements Review and Mission Definition Review in November 2013
  Passed KDP-B April 2014, now in Phase B
  Most technical issues solved at the preliminary design level, following technical interchange meeting at Ball, April 2014
  Passed PDR on July 31, 2014
  KDP-C scheduled for November, 2014
  Detectors in-house, grating and optical bench ordered
  Ground systems development at SAO on schedule
Satellite host selection and Instrument CDR summer 2015
  TEMPO operating longitude and launch date are not known until after host selection
Instrument delivery 05/2017 for launch 11/2018 or later

## Slide 24: The end!

## Slide 25: Backups

## Slide 26: TEMPO science traceability matrix

## Slide 27: Baseline and threshold data products
Species/Products | Required Precision | Temporal Revisit
0-2 km O3 (Selected Scenes) Baseline only | 10 ppbv | 2 hour
Tropospheric O3 | 10 ppbv | 1 hour
Total O3 | 3% | 1 hour
Tropospheric NO2 | 1.0 × 1015 molecules cm-2 | 1 hour
Tropospheric H2CO | 1.0 × 1016 molecules cm-2 | 3 hour
Tropospheric SO2 | 1.0 × 1016 molecules cm-2 | 3 hour
Tropospheric C2H2O2 | 4.0 × 1014 molecules cm-2 | 3 hour
Aerosol Optical Depth | 0.10 | 1 hour
PLRA Table 1
Minimal set of products sufficient for constraining air quality
Across Greater North America (GNA): 18°N to 58°N near 100°W, 67°W to 125°W near 42°N
Data products at urban-regional spatial scales
  Baseline ≤ 60 km2 at center of Field Of Regard (FOR)
  Threshold ≤ 300 km2 at center of FOR
Temporal scales to resolve diurnal changes in pollutant distributions
Collected in cloud-free scenes
Geolocation uncertainty of less than 4 km
Mission duration, subject to instrument availability
  Baseline 20 months
  Threshold 12 months

## Slide 28: Data product definitions and details
Data Product | Description | Time beyond on-orbit checkout to deliver initial data | Maximum data latency after first release for ≥ 80% of all products†
Level 0 | Reconstructed, Unprocessed Instrument Data | 2 months | Within 2 hours of receipt at SAO
Level 1b | Calibrated, Geolocated Radiances | 4 months | Within 3 hours of Level 0 and ancillary data receipt at SAO
Level 2 | Derived Geophysical Data Products | 6 months | Within 24 hours of production of Level 1 at SAO
Level 3 | Derived Gridded Geophysical Data Products | 6 months | 1 month after completion of data accumulation required for individual geophysical products
All original observation data and standard science data products listed here, along with the scientific source code for algorithm software, coefficients, and ancillary data used to generate these products, shall be delivered to the designated NASA SMD/ESD-assigned DAAC within six months of completion of the prime mission. Data products are publicly distributed during the mission.
†80% of the products, not 80% of the product types, will be produced within this latency time.

## Slide 29: Instrument Functional Block Diagram
2416398 Rev. C

## Slide 30: TEMPO