## Slide 1: UV/VIS backscattered Sun light retrievals from space born platforms
G. Gonzalez Abad
With a lot of help from K. Chance, X. Liu, C. Miller and others

## Slide 3: Overview
A bit of history on UV-VIS backscatter spectrometers
  Past, present and future instruments (as far as I know)
  TOMS vs. OMI
  GOME vs. OMI
  The GEO constellation
Slant column retrievals
  The equations: BOAS
  To have in mind (solar spectrum, cross sections, ring, undersampling, …)
  Examples
Slant column to vertical column
  Equations
Vertical columns: examples from OMI

## Slide 4: History: The DISCOVERY OF THE ozone hole fuelled the interest in the atmospheric chemistry and composition during the 1970s
USA
Europe

## Slide 5: HISTORY & PRESENT: USA
Instrument | Satellite (Agency) | Period
BUV | Nimbus-4 (NASA) | 1970-1980
SBUV | Nimbus-7 (NASA) | 1978-1993
TOMS | Nimbus-7 (NASA) Meteor-3 (NASA) (Russian) Earth Probe (NASA) | 1978 1993 1996-2007
SBUV/2 | NOAA 9,10,11,13,14,17,16,18,19 (NOAA) | 1984 – present
OMI | AURA (NASA/KNMI) | 2004-present
OMPS | SUOMI-NPP (NOAA) | 2011-present

## Slide 6: HISTORY & PRESENT: Europe & CHINA
Instrument | Satellite (Agency) | Period
GOME | ERS-2 (ESA) | 1995-2011
SCIAMACHY | ENVISAT (ESA) | 2002-2012
OMI | AURA (KNMI/NASA) | 2004-present
GOME2 | Metop-A (EUMETSAT) Metop-B (EUMETSAT) | 2006-present 2012-present
TOU/SBUS | FY-3A (NRSCC) FY-3B (NRSCC) FY-3C (NRSCC) | 2008-present

## Slide 7: Future instruments
Instrument | Satellite (Agency) | Orbit
OMPS | JPSS1 (NOAA) JPSS2 (NOAA) | LEO LEO
TROPOMI | SENTINEL 5P (ESA) | LEO
GOME-2 | Metop-C (EUMETSAT) | LEO
UVAS | Seosat-Ingenio (CDTI) | LEO
UVN | SENTINEL 4 (ESA) | GEO
GEMS | MP-GEOSAT (KORA) | GEO
TEMPO | TBD (NASA/SMITHSONIAN) | GEO

## Slide 8: Toms vs. omi
 | TOMS (Nimbus-7) | OMI
Spectral coverage | 312.5 nm 317.5 nm 331.3 nm 339.9 nm 360.0 nm 380.0 nm | UV1: 270-314 nm UV2: 306-380 nm VIS: 350-500 nm
Bandwidth, resolution | 1.1 nm | 0.63 – 0.45 nm
Ground pixel size (nadir) | 50 x 50 km2 | 13 x 24 km2
Global coverage | Daily | Daily

## Slide 9: GOME vs. OMI
Photodiode detectors 1024 pixels
GOME
OMI
2D CCD detector

## Slide 10: THE GEO CONSTELLATION
& Kelly Chance

## Slide 11: Slant column retrieval

## Slide 12: Slant column retrieval

## Slide 13: SLANT COLUMN RETRIEVAL: BOAS

## Slide 14: SLANT COLUMN RETRIEVAL: Irradiance
OMI irradiance, Dobber at al. 2006

## Slide 15: SLANT COLUMN RETRIEVAL: ring spectrum
Chance and Kurucz
2010

## Slide 16: SLANT COLUMN RETRIEVAL: Undersampling
Chance et. Al, 2005

## Slide 17: SLANT COLUMN RETRIEVAL: cross sections

## Slide 18: SLANT COLUMN RETRIEVAL: common mode

## Slide 19: SLANT COLUMN RETRIEVAL: optical depth
Courtesy: IUP-IFE, University of Bremen

## Slide 20: SLANT COLUMN RETRIEVAL: HIGH resolution solar spectrum
Chance & Kurucz, 2010

## Slide 21: SLANT COLUMN RETRIEVAL: SLIT FUNCTION
Dirksen et al. 2006

## Slide 22: SLANT COLUMN RETRIEVAL: i0 correction
Wagner, Chance et al.

## Slide 23: Slant column retrieval: OMI C2HO

## Slide 24: Slant column retrieval: OMPS NO2

## Slide 25: Slant column retrieval: OMPS C2HO

## Slide 26: Vertical column: equations
AMF (Air Mass Factor)

## Slide 27: Vertical column: equations
w(z) Scattering weights from Vlidort
Sx (z) shape factors from a climatology for example GEOS-Chem

## Slide 28: Vertical column: equations, Shape factors

## Slide 29: Vertical column: EQUATIONS scattering weights
Cloudy SZA: 28°
Clear SZA: 24°
Clear VZA: 2.7°
Cloudy VZA: 16°
Clear cloud fractions: 0.01
Cloudy cloud fraction: 0.2

## Slide 30: Vertical column: equations SINGEL PIXEL approximation

## Slide 31: Generic retrieval framework
Typical retrieval flow chart for a retrieval
L1 data
Auxiliary data
Read L1 data
Read auxiliary data
Wavelength calibration using high resolution solar spectrum
Compute AMFs
Compute I0 correction
Compute Common mode spectrum
Compute under sampling spectrum
Direct fitting of slant columns
Read look up tables & climatology
Compute vertical columns
Compute Ring spectrum
Post processing (if needed)
Look up tables and climatology for AMF calculation

## Slide 32: VERTICAL column retrieval: OMI C2HO

## Slide 33: VERTICAL column retrieval: OMI Bro

## Slide 34: VERTICAL column retrieval: OMI C2H2O2

## Slide 35: VERTICAL column retrieval: OMI H2O
20050714
20070714
20110714
20130714

## Slide 36: THE END
PLUS TEAM HANDBALL

## Slide 37
OMI operational HCHO
Fitting window | 327.5 – 356.5 nm
Baseline polynomial | 3rd order
Scaling polynomial | 3rd order
Instrument slit function | Hyper-parameterization of pre-flight measurements
Wavelength calibration | Spectral shift (no squeeze)
Solar Reference Spectrum | Chance and Spurr, 1997
HCHO cross sections | Cantrell et al., 1990; 300K
O3 cross sections | Macilet et al., 1995; 228K
NO2 cross sections | Vandaele et al., 1998 220K
BrO cross sections | Wilmouth et al., 1999; 228K
Molecular Ring cross sections | Chance and Spurr, 1997
Sampling correction | Computed on-line
Residual common mode spectrum | Computed on-line

## Slide 38: OMI CHOCHO
Fitting window | 431.5 – 469.5 nm
Baseline polynomial | 4th order
Scaling polynomial | 3rd order
Instrument slit function | Hyper-parameterization of pre-flight measurements
Wavelength calibration | Spectral shift (no squeeze)
Solar Reference Spectrum | Chance and Spurr, 1997
CHOCHO cross sections | Volkamer et al., 2005; 296K
O3 cross sections | Macilet et al., 1995; 228K
NO2 cross sections | Vandaele et al., 1998 220K
O2-O2 cross sections | Hermans BISA, 2006; 294K
H2O cross sections | HITRAN 2008, 280K
Liquid H2O cross sections | Pope and Fry, 1997
IO cross sections | Spietz et al., 2005; 298K
Vibrational Raman Spectrum | Chance and Spurr, 1997
Molecular Ring cross sections | Chance and Spurr, 1997
Sampling correction | Computed on-line
Residual common mode spectrum | Computed on-line

## Slide 39
OMI operational BrO
Fitting window | 319.0 – 347.5 nm
Baseline polynomial | 4rh order
Scaling polynomial | 4th order
Instrument slit function | Hyper-parameterization of pre-flight measurements
Wavelength calibration | Spectral shift (no squeeze)
Solar Reference Spectrum | Chance and Spurr, 1997
HCHO cross sections | Cantrell et al., 1990; 300K
O3 cross sections | Macilet et al., 1995; 218K; 295K
NO2 cross sections | Vandaele et al., 1998 220K
BrO cross sections | Wilmouth et al., 1999; 228K
O2-O2 cross sections | Hermans BISA, 2006; 294K
SO2 cross sections | Hermans et al., 2009; 295K
OClO cross sections | Kromminga et al,. 2003; 213K
Molecular Ring cross sections | Chance and Spurr, 1997
Sampling correction | Computed on-line
Residual common mode spectrum | Computed on-line

## Slide 40
OMI operational OClO
Fitting window | 358.5 – 392.0 nm
Baseline polynomial | 3rd order
Scaling polynomial | 3th order
Instrument slit function | Hyper-parameterization of pre-flight measurements
Wavelength calibration | Spectral shift (no squeeze)
Solar Reference Spectrum | Chance and Spurr, 1997
O3 cross sections | Macilet et al., 1995; 228K
NO2 cross sections | Vandaele et al., 1998 220K
BrO cross sections | Wilmouth et al., 1999; 228K
O2-O2 cross sections | Hermans BISA, 2006; 294K
OClO cross sections | Kromminga et al,. 2003; 213K
Molecular Ring cross sections | Chance and Spurr, 1997
Sampling correction | Computed on-line
Residual common mode spectrum | Computed on-line

## Slide 41
GOME2 SO2
Fitting window | 312.0 – 330.0 nm
Baseline polynomial | 3rd order
Scaling polynomial | 3rd order
Instrument slit function | Asymmetric Gaussian fitted online
Wavelength calibration | Spectral shift (no squeeze)
Solar Reference Spectrum | Chance and Spurr, 1997
SO2 cross sections | Bogumil et al., 2003; 293K
HCHO cross sections | Meller and Moortgat et al., 2000; 298K
O3 cross sections | Brion et al., 1993; 218K, 273K
NO2 cross sections | Vandaele et al., 1998 220K
BrO cross sections | Wilmouth et al., 1999; 228K
Molecular Ring cross sections | Chance and Spurr, 1997
Sampling correction | Computed on-line
Residual common mode spectrum | Computed on-line